## Slide 1
Dynamic Host Configuration Protocol

## Slide 2
Overview

## Slide 3: This session
We are going to talk about:
  Introduction to DHCP
  DHCP client
  DHCP server

## Slide 4: Introduction to DHCP(I)
Dynamic Host Configuration Protocol
DHCP is a protocol used by Networked devices to obtain several parameters necessary for the clients.
DHCP can be used to automatically assign IP addresses, to deliver TCP/IP stack configuration parameters such as the subnet mask and default router, and to provide other configuration information.

## Slide 5: Introduction to DHCP(I)
DHCP is based in an architecture “Client-Server” where:
  Client asks for information
  Server answers with the information it has.
DHCP works in port 67/UDP for the server side and 68/UDP for the client side.

## Slide 6: Introduction to DHCP (II)
DHCP has different methods for IP addresses allocation:
  dynamic_allocation: A network manager assigns a range of IP to DHCP. The server leases the IP during some time.
  automatic_allocation: The DHCP server permanently assigns a free IP address to a requesting client from the range defined by the administrator.
  manual_allocation: The DHCP server allocates an IP address based on a table with MAC address.

## Slide 7: Introduction to DHCP (III)
DHCP has several messages:
  DHCP discovery: The client multicasts on the physical subnet to find available servers.
  DHCP offers: When a DHCP server receives an IP lease request from a client, it extends an IP lease offer.
  DHCP requests: The client accepts the offer.
  DHCP acknowledgement: Final phase.

## Slide 8: Introduction to DHCP (III)
Typical sequence diagram:

## Slide 9: Introduction to DHCP (III)
Other messages:
  DHCP release: The client releases the IP.
  DHCP information: Requests more information than the server sent with the original DHCPACK
RFC:
  ftp://ftp.isi.edu/in-notes/rfc2131.txt

## Slide 10: DHCP server (I)
Installation
  yum install dhcpd
  service dhcpd start ( centos 6 )
  systemctl start dhcpd ( centos 7 )
configuration file
  /etc/dhcpd.conf
Ports
  UDP/67
  UDP/68

## Slide 11: DHCP server (II)
Configuring dhcpd.conf:
  “option”: you can define common options for all supported networks. For example:
option domain-name “mswl.com”
option domain-name-servers ns1.mswl.com ns2.mswl.com
  “authoritative”: Example of use, your laptop has a old IP (from one subnet) from your home and you are at the office (other subnet). If you want to force to forget the old IP you need this configured.
  subnet: directive for defining subnet configuration.

## Slide 12: DHCP server (III)
Configuring dhcpd.conf:
  shared-network: directory for defining IP subnets that actually share the same physical network.
  host: There must be at least one host statement for every BOOTP client that is to be served.
  group: The group statement is used simply to apply one or more parameters to a group of declarations.

## Slide 13: DHCP server (III)
First example, assigning IP addresses randomly:
  option subnet-mask 255.255.255.0; #Its subnet mask
  option broadcast-address 192.168.1.255; #Client should use this IP as Broadcast.
  option routers 192.168.1.254; #Is the router/gateway
  option domain-name-servers 192.168.1.1, 192.168.1.2; #Its DNS servers
  option domain-name "mswl.com";
  subnet 192.168.1.0 netmask 255.255.255.0 {
  range 192.168.1.10 192.168.1.100; # One of this range will be offered
  range 192.168.1.150 192.168.1.200; # Or one of this range will be offered
}

## Slide 14: DHCP server (III)
Second, assigning fixed IP addresses to known hosts:
default-lease-time 6000; # It will lease an IP address for 600 seconds if the client doesn't # ask for specific time frame
max-lease-time 7200; # The maximum (allowed) lease will be 7200 seconds
subnet 192.168.1.0 netmask 255.255.255.0 { #Declares a subnet...
option domain-name "mswl.com";
option domain-name-servers 192.168.1.1, 192.168.1.2; #Its DNS servers
option routers 192.168.1.3;
host myhostname {
hardware ethernet 00:00:00:00:00:00; # MAC address for host
fixed-address 192.168.1.4; # This IP will be assigned to myhostname.
}
}

## Slide 15: DHCP server (III)
With the server configured:
  The file “dhcpd.leases” should be created if doesn't exists.
touch /var/lib/dhcp3/dhcpd.leases ## In Ubuntu this file exists... and contains all the
## assigned information: ip, dns, etc.
  You can now start the server:
/etc/init.d/dhcp3-server restart
  See more info:
http://www.isc.org/index.pl?/sw/dhcp/dhcpv3-README.php
http://tldp.org/HOWTO/DHCP/index.html
http://www.arda.homeunix.net/dnssetup.html

## Slide 16: DHCP client (I)
DHCP needs configuration of server and client.
DHCP client in Ubuntu:
apt-get install dhcp3-client dhcp3-common
The dhcpcd package installs it's startup script as usual for debian packages in /etc/init.d/package_name, here as /etc/init.d/dhcpcd, and links this to the various /etc/rcX.d/ directories.

## Slide 17: DHCP client (II)
In order to configure one interface (for example, eth0) with dhcp you need to add to “/etc/network/interfaces” this line:
  auto: the interface should be configured during boot time.
  inet: interface uses TCP/IP networking.
  dhcp: the interface can be configured through DHCP.
auto eth0
iface eth0 inet dhcp

## Slide 18: DHCP client (III)
If you don't want to use DHCP you could add static configuration:
iface eth0 inet static
address 192.168.12.2
netmask 255.255.255.0
gateway 192.168.12.254

## Slide 19: DHCP client (IV)
A view to dhclient.conf:
  retry: Time to determine if there isn't server.
  reboot: dhcp first tries to reacquire the last address it had, this is the time to try to reacquire the old IP.
  request: Options that the client requests to receive in an offer.
  require: Options that the client requires to accept an offer.
  send: Client send the specified options.
  lease: For alternate database after timing.

## Slide 20: DHCP client (V)
The options are in “man dhcp-options”. Some of them:
  option subnet-mask: Clients subnet mask.
  option routers: Router on the client subnet.
  option domain-name-servers: List of domain name servers.
  option domain-name: Domain name that client should use when resolving hostnames via the Domain Name System.

## Slide 21: DHCP client (V)
Example of configuration:
timeout 60; # time between begins and the time that it decides that it's not going
# to contact with the server
retry 60;
reboot 10; # Seconds to maintain old IP in a reboot.
select-timeout 5; # select-timeout has expired, the client will accept the first offer
reject X.X.X.X; #Rejects offers from this IP as server.
alias { #While roaming forcing that the client has an alias with fixed IP.
interface "eth0";
fixed-address 192.5.5.213;
option subnet-mask 255.255.255.255;
}

## Slide 22: DHCP client (V)
Continuation of example:
lease {
interface "eth0";
fixed-address 192.33.137.200; #Old IP given by below router
option host-name "MyHostnameOnNetwork"; #Host name
option subnet-mask 255.255.255.0; # Subnet mask
option broadcast-address 192.33.137.255;
option routers 192.33.137.250; #Router with it will try to contact to bind with IP
option domain-name-servers 127.0.0.1;
renew 2 2008/4/12 00:00:01; #Time to try to contact with its server.
rebind 2 2008/4/12 00:00:01; #Time to try to contact with any server.
expire 2 2008/4/12 00:00:01; # Client must stop using a lease if it has not been
# able to contact a server in order to renew it.
}